## Slide 1
PWP data flow
Inputs
MET Data (2 structures with arrays length(time) x 1)
fluxes.sw_net – shortwv radiation
fluxes.lw_net - longwv radiation
fluxes.hsb – sensible heat flux
fluxes.hlb – latent heat flux
fluxes.tau – wind stress (scaler)
SWIFT – “.winddir” (CCW 0 deg north) and “.time” (datenum)
Initial Profile Data (1X1 structure with arrays length(z) x 1)
profile.time [julian datenum]
profile.z [m] – depth positive down
profile.t [deg C] - Temperature
profile.s [PSU] – Salinity
Define Setup Parameters (see page 3) and setup model grid
Time Stepped Loop
pwpgo(…) – applies surface fluxes to all cells starting at the top
1. t(1) = (qi*absrb(1) + qo) * dt / (dz * d(1) * cpw) – Updates top cell temp.
where qi is sw rad and qo is lw - qlat - qsens.
2. s(1) = s(1)/(1-emp*dt/dz) – Updates top cell freshwater flux using evap. minus precip. rate (emp). Evaporation calculated from qlat.
3. t(2:end) = absrb(…) – calculates penetrating sw rad. into interior cells and calculates new “t” profile
4. Recompute density
5. remove_si(…) – removes static instability simulating convective overturning.
6. Find a mixed layer depth (MLD) using drho/dz threshold.
7. Apply momentum flux uniformly over MLD such that du = (tx/(ml_depth*d(1)))*dt. Use coriolis to find angle between tau_x and u.
8. Apply inertial/inertial wave damping.
9. Apply bulk richardson number mixing up to rb (page 3)
10. Apply gradient richardson number up to rg (page 3)
**Fluxes same sign convention as COARE (lw and sw (+) heating ocean, sen and lat (-)

## Slide 2
PWP data flow
Outputs
Output Data (1X1 structure with arrays length(time) x 1)
pwp_output.time [julian datenum] – mxn timegrid
pwp_output.t [deg C] – mxn temperature grid
pwp_output.s [PSU] – mxn salinity grid
pwp_output.d [kg/m^3] – mxn density grid
pwp_output.u [m/s] – mxn eastward velocity grid
pwp_output.v [m/s] – mxn westward velocity grid
pwp_output.mld [m] – 1xn mixed layer depth
pwp_output.dt [s] – 1x1 timestep size
pwp_output.dz[m] – 1x1 depthstep size
pwp_output.lat [deg] – 1x1 latitude
Matlab functions on GitHub at
https://github.com/SASlabgroup/SWIFT-codes/tree/a467fd08e1d11a6182c9b3a000679a8d8cba7159/GeneralTools/PWP1986
Derived from
git@github.com:earlew/pwp_python_00.git

## Slide 3
Setup Parameters
Variable | Definition | Units | Role in Model
dt | Time-step increment | s | Main timestep used in time loop (dt = 1 → 1 day). Used for all flux integrations.
dz | Depth increment | m | Vertical grid spacing for z = 0:dz:depth. Controls model resolution.
depth | Maximum model depth | m | Total depth of the model domain. Truncated to match profile if shallower.
dt_save | Save interval multiplier | — | Number of timesteps per save output (e.g. 1 → save every step).
lat | Latitude | ° | Used to compute Coriolis parameter f = gsw_f(lat).
g | Gravitational acceleration | m s⁻² | Used in Richardson number and buoyancy calculations (9.81).
cpw | Specific heat capacity of seawater | J kg⁻¹ °C⁻¹ | Converts surface heat flux (W m⁻²) into temperature tendency: ΔT = Q dt / (ρ cp Δz).
f | Coriolis frequency (from latitude) | s⁻¹ | Determines inertial oscillations and rotation of velocity vectors.
ucon | Inertial/internal wave damping coefficient | s⁻¹ | Small parameter (~0.1 ×
rkz | Background vertical diffusivity | m² s⁻¹ | Optional constant vertical diffusion coefficient for scalar fields. If 0 → disabled.
dstab | Diffusive CFL number | — | dstab = dt * rkz / dz²; must be ≤ 0.5 for stability.
diagnostics | Diagnostic flag | (0–3) | Controls plotting mode during run (0 = none, 1 = profiles & KE, 2 = momentum, 3 = MLD).
rb | 0.65 | dimensionless | Critical bulk Richardson number for entrainment (bulk Ri threshold).
rg | 0.25 | dimensionless | Critical gradient Richardson number for shear (local) mixing.
rkz | 0 | m² s⁻¹ | Background vertical diffusivity (if >0, diffus operator is called).
beta1 | 0.6 | m | Short (red) extinction scale for solar absorption (shallow/strong absorption).
beta2 | 20 | m | Long (blue) extinction scale for solar absorption (deeper penetration).